## Slide 1: HI² Hypervisor international /In-House
28/11/2025

## Slide 2: Hardware architecture Current situation in Italy Current situation in France
Overview
HI² Benefits
In Italy
deployment to production Adaptation to France
Planning previw

## Slide 3: Hardware architecture
Plant
Circuit breaker
Circuit breaker
Circuit breaker
Thytronic
Thytronic
Thytronic
Current situation in Italy
Inverters
Network 1
Router
…
…
Network 2
VPN Access Integration
In order to get secure remote access a vpn
could be installed in the router
Modem
Currently, Thytronics are monitoring
the plant automatically with a threshold on the meter.
If any issue occurs, the Thytronic must be reset
and the plant manually reconnected.

## Slide 4: Hardware architecture
Antena
PDL
PTR
Mini-PC
Modem 3G/4G
Automate Master
Switch
12V/24V
Battery 12V
Enedis
Automate slave
Switch
Battery au Pb 12V
Frontiere
box
DEIE
48V
Alim 230V
230/24V
24V
12V
Alim
RJ45
Coaxial
standard Wire
12V
Cell
protection
Motor
Alim 230V
48V
48V
24V
Current situation in France

## Slide 5: Hardware architecture
Current situation in France
Mini-PC
192.168.1.30
Modem 3G/4G
192.168.1.1
Automate Master
192.168.1.17 (wago) 192.168.1.4(siemens)
Automate slave
DEIE
PC
Hyperviseur
Smartlogger
(192.168.1.100)
Inverter
(192.168.1.101
192.168.1.102
…
192.168.1.110
…)
Server Broker
MQTT
MQTT
Powered by

## Slide 6: HI² Hypervisor in house

## Slide 7: HI²
Benefits
Cost-free, fully developed in-house
Secured by credentials, Microsoft Entra, and VPN
Access can be easily granted to the O&M contractor.
They will be able to give feedback on their action.
And recouple instantly managing the error at distance,

## Slide 8: HI²
In Italy
Navigateur web
Front: Next.js
Backend: Node/Express
Polling service: Node.js
Base de données: SQL Lite
API : Port 3001
HTTPS : Port 3000
Thytronics
Control
Modbus/TCP

## Slide 9: HI²
In Italy (what’s next ?)
Next development:
Modbus Reading Siprotec 7SJ80
Alarm to be sent via email
or SMS
Final solution expected to be delivered in February/March 2026

## Slide 10: HI²
deployment to production
Run logic on Virtual machine (the same that it used to host VPN for plant):
Managed by IT. It will be in charge to maintain server launch relaunch web app
Accessible by VPN
HI² will be deployed and update/upgrade by IoT team because it will be simple it will be deployed under docker

## Slide 11: HI²
In France
Mini-PC
192.168.1.30
Modem 3G/4G
192.168.1.1
Automate Master
192.168.1.17 (wago) 192.168.1.4(siemens)
Automate slave
DEIE
PC
Smartlogger
(192.168.1.100)
Server Broker
MQTT
MQTT
MQTT
Inverter data

## Slide 12: HI²
In France
Backlog to be defined
Development to be planned for Operations
Modification of the Synoptic Menu
Modification of the Inverter Menu
Creation/Modification of plant declarations
Navigateur web
Front: Next.js
Backend: Node/Express
Polling service: Node.js
Base de données: MongoDB
API : Port 3001
HTTPS : Port 3000
Server Broker
OU

## Slide 13: HI²
deployment to production
1
Q4 2025
Current testing and validation phase in Italian pilot sites, gathering operational data and refining core functionality.
2
Q1 2026
Development completion with Thytronic reset, circuit breaker monitoring, and alarm system implementation.
3
Feb-Mar 2026
Final solution delivery for Italy with full remote management capabilities and production-ready status.
4
Q2 2026
Adaptation and deployment planning for French operations, leveraging lessons learned from Italian rollout.
5
Feb-Mar 2026
Retrofit ending, deplyement of the inhouse hypervisor